## Slide 1
DATA-DRIVENSOLAR
AEROPONICS
DESIGN, BUILD, AND IMPLEMENTATION PLAN
Project Lead: Jaime Conde and Shazia Khan
Team: Flora, Torrin, Citlaly, Luke

## Slide 2
Goal of this meeting:
OBJECTIVE
  Finalize required materials and identify missing components
  Assign clear roles and responsibilities for each subsystem
  Establish a realistic build timeline and work location
  Confirm team commitment, availability, and long-term ownership

## Slide 3
SYSTEM OVERVIEW
  Vertical aeroponic growing system
  Soil-free, mist-based root nourishment
  Sensor-driven (pH, TDS, temperature)
System Type
  LED grow lights
Lighting
  Nutrient solution
  Doser pumps
  Net cups + growing medium
Nutrients
  PVC frame + vertical columns
  Reservoir tanks
Structure
  Water pumps
  Tubing + mist nozzles
  Flow meters
Flow System
  Raspberry Pi
  Sensors (pH, TDS, water level, light)
  Relay module + power supply
Control System
  Solar panel (Optional)
  battery
  controller (Optional
Energy

## Slide 4
RISKS AND MITIGATION
  Pump Failure (Flow System)
→ Loss of mist → plants die within ~30 minutes
Solution:
  Use reliable pump (rated continuous use)
  Keep backup pump available
  Test before full operation
  Clogged Tubing / Nozzles
→ Uneven or no nutrient delivery
Solution:
  Use filtered water
  Regular cleaning schedule
  Easy-access tubing design
  Power Failure
→ Entire system shuts down
Solution:
  Add battery backup (later phase)
  Manual check schedule
  Alert system (future upgrade)
System Failure Risks
  Sensor Failure (pH / TDS / Water Level)
→ Incorrect nutrient conditions
Solution:
  Manual verification (weekly)
  Calibrate sensors regularly
  Redundant checks (visual + measurement)
  Relay / Electrical Failure
→ Pump or system not triggered
Solution:
  Test wiring before deployment
  Use fused connections
  Keep spare relay module
Measurement & Control Risks
  No Summer Maintenance
→ System dries out and fails
Solution:
  Assign weekly maintenance roles
  Create schedule before build
  Transfer ownership if needed
  Delayed Structure Build
→ Entire project timeline pushed back
Solution:
  Prioritize structure materials first
  Assign structure lead
  Set early build deadline
Project Execution Risks

## Slide 5
BOM

## Slide 6
TOOLS AND SPONSORSHIPS

## Slide 7
BUILD PROCESS

## Slide 8
ROLES AND RESPONSIBILITIES
THIS CHART IS MEANT AS A GENERAL REPRESENTATION OF WHAT TASKS NEED TO BE DONE, NOT A STRICT ASSIGNMENT SHEET. I ENCOURAGE PEOPLE TO WORK TOGETHER IN AN INTERCONNECTED WAY. IF WE KNOW SOMEONE WILL BE GONE FOR A SPECIFIC WEEK/TIME PERIOD WE CAN MOVE AROUND WHO DOES WHAT.